| Air flow at nominal condition 1 | 760 Nl/min – 45,6 Nm3/h – 27 Scfm |
| --- | --- |
| Pressure DewPoint at nominal condition 2 | -20 °C, -40 °C o -70 °C |
| Nominal ambient temperature | 1 - 50 °C |
| Nominal inlet air temperature | 35 °C |
| Max. inlet air temperature | 50 °C |
| Nominal inlet air pressure | 7 barg |
| Max. inlet air pressure | 16 barg |
| Inlet-outlet air connection | G 3/8” BSP-F |
| Desiccant type and quantity | Molecular Sieve – 12,0 kg |
| Power supply | 1/230-240V/50-60Hz |
| Electric consumption | 50 W |
| Weight | 71 kg |

1 The nominal condition refers to an inlet air at 7 barg and 35°C.

2 Specify it, at ordering confirmation.

| Correction factor for operating pressure changes : |
| --- |
| Inlet air pressure barg | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 |
| Correction factor | 0.62 | 0.77 | 0.90 | 1.00 | 1.09 | 1.17 | 1.24 | 1.31 | 1.37 | 1.42 | 1.47 | 1.52 | 1.56 |

| Correction factor for inlet air temperature changes : |
| --- |
| Air temperature ºC | < 25 | 30 | 35 | 40 | 45 | 50 |
| Correction factor | 1.12 | 1.06 | 1.00 | 0.93 | 0.86 | 0.78 |